## Slide 1: Design of a RLNC implementation on the switch

## Slide 2: Modules
Buffering Module
Network Coding Module
Recoding submodule
Coding Submodule
Decoding Module
Forwarding Module

## Slide 3
Buffering Module
Buffering Module
Core objective:
  To store the symbols in the switch needed for future encoding opportunities.
Challenges:
  Indexing the symbols.
  Keeping track of where each symbol is.
  Handling a large number of symbols
    No loops, can’t iterate over registers
    No way to efficiently fetch the necessary symbols
Solutions:
  Implementation of a circular buffer, to re-use space.
  Index the symbols based on its generation, separately allocate buffer space for each different generation.
  Limit the number of symbols that can be buffered at the same time

## Slide 4
Network Coding Module
Core objective:
  To implement a Random Linear Coding solution on the switch’s data plane.
Design Choice N.º1 – Choosing the type of RLNC:
  Generation based RLNC
    More common
    High in-order delivery delay
    Multiple approaches to implement this (e.g. multigeneration,
    Need to create generations
  Sliding Window RLNC
    Newer approach to RLNC
    Good for streaming applications
    Low in-order delivery delay
Network Coding Module

## Slide 5
Network Coding Module
Design Choice N.º2 – Defining the parameters
  Finite Field Size
    Large field
      Lower risk of linearly dependent packets
      Increased implementation complexity
    Small Field
      Higher risk of linearly dependent packets
      Lower implementation complexity
    , is the most commonly used.
  Generation Size – How many packets are coded together:
    Large Generations Sizes
      Higher Delay/Throughput/Complexity
    Small Generation Sizes
      Lower Delay/Throughput/Complexity
Network Coding Module

## Slide 6
Network Coding Module
Coding Submodule
Coding Submodule
Main functions:
  To code original symbols and generate enough coded symbols for the decoding process.
  To generate random coefficients.
  To perform the required linear combinations.
Design choice N.º3 – Where to generate the coded packets
  Coded Packets are usually generated at the source
  Host
  Switch
Design choice N.º4 – Is there a need for feedback
  Can be used to know when to stop generating coded packets
Design choice N.º5 – How implement product/division
  Lookup tables
    Good for smaller finite fields (e.g. )
    Needs the appropriate memory space
    Doesn’t work with larger finite fields, the memory space required is too much
  Others
    Product (shifts+ XORs)
    Modulo irreducible polynomial (long division)

## Slide 7
Network Coding Module
Recoding Submodule
Recoding Submodule
Main functions:
  To code once again the coded symbols.
  To update the coding coefficients.
  To update the coded symbols.
Same design choices as the coding submodule

## Slide 8
Network Coding Module
Decoding Submodule
Decoding Submodule
Main functions:
  To decode the coded symbols, producing the originals ones.
  To check for linear independency
  To perform Gaussian Elimination
Design choice N.º6 – Checking for linear independency
  Possible on a switch?
Design choice N.º7 – Solving the linear equations (decoding)
  Possible on a switch?

## Slide 9
Forwarding Module
Core objective:
  To forward the packet to the next node according to some forwarding policy
Forwarding Module

## Slide 10: References
S. Wunderlich, F. Gabriel, S. Pandi, F. H. P. Fitzek and M. Reisslein, "Caterpillar RLNC (CRLNC): A Practical Finite Sliding Window RLNC Approach," in IEEE Access, vol. 5, pp. 20183-20197, 2017. doi: 10.1109/ACCESS.2017.2757241
M. V. Pedersen, D. E. Lucani, F. H. P. Fitzek, C. W. Sørensen and A. S. Badr, "Network coding designs suited for the real world: What works, what doesn't, what's promising," 2013 IEEE Information Theory Workshop (ITW), Sevilla, 2013, pp. 1-5.
Torre R., Pandi S., Fitzek F.H.P. (2019) Network-Coded Multigeneration Protocols in Heterogeneous Cellular Networks. In: Sucasas V., Mantas G., Althunibat S. (eds) Broadband Communications, Networks, and Systems. BROADNETS 2018. Lecture Notes of the Institute for Computer Sciences, Social Informatics and Telecommunications Engineering, vol 263. Springer, Cham