## Slide 1: Design of a RLNC implementation on the switch

## Slide 2: Modules
Buffering Module
Network Coding Module
Recoding Module
Coding Module
Decoding Module
Forwarding Module

## Slide 3
Buffering Module
Buffering Module
Core objective:
  To store the symbols in the switch needed for future encoding opportunities.
Challenges:
  Indexing the symbols.
  Keeping track of where each symbol is.
  Handling a large number of symbols
Solutions:
  Implementation of a circular buffer, to re-use space.
  Index the symbols based on its generation, separately allocate buffer space for each different generation.
  Limit the number of symbols that can be buffered at the same time
Implementation:
  Through the use of registers it’s possible to store the symbols in the switch.

## Slide 4
Network Coding Module
Network Coding Module
Core objective:
  To implement a Random Linear Coding solution on the switch’s data plane.
Challenges:
  Defining important parameters
    Finite Field Size
    Generation Size
    Symbol Size
  Deciding on which type of RLNC to implement, such as Generation based RLNC or Sliding Window RLNC
Solutions:
  Depends on the capabilities of the device, memory available, computation power.
  ???

## Slide 5
Network Coding Module
Coding Module
Coding Module
Core objective:
  To code original symbols and generate enough coded symbols for the decoding process.
Implementation:
Challenges:
  Performing multiplication
  Handling arithmetic operations with a large number of symbols and coefficients leads to a more complex computation.
Solutions:
  Use lookup tables for multiplication
  ???